## Slide 1
SMART IoT
IoT
PROJECT
3
Environmental Monitoring
Using Robustel EG5120 Gateway and S6000U Sensor
Machine Learning Edge Intelligence | Telecommunication Engineering Program
Sisay Desalegn • Yonas Yifter • Zakariye Hassan • Meron Temesgen • Jhena Subol • Husayn Ismail • Rima Kasem
Supervisor: Prof. Vincenzo Barbuto | UNICAL | February 2026
UNICAL • 2026

## Slide 2
Presentation Overview
Agenda
01
Project Introduction
02
System Architecture
03
Hardware Components
04
Software Stack
05
Machine Learning
06
Web Platform & Chatbot
07
Testing & Deployment
08
Conclusion
Smart IoT Environmental Monitoring | Giganti della Sila Park | Telecommunication Engineering Program

## Slide 3
Project Introduction
Giganti della Sila Park — Calabria, Italy
Background
Giganti della Sila is a protected mountain park in Calabria, Italy, known for its ancient pine forests, hiking trails, and scenic viewpoints.
No real-time environmental intelligence
Limited predictive visitor guidance
Manual park management systems
The Smart Park Solution
An IoT-driven ecosystem enabling:
🌡 Continuous environmental monitoring
🤖 AI-based trail recommendations
📍 Safety alerts & localization
💬 Virtual assistant support
📊 Data-driven operational decisions
Smart IoT Environmental Monitoring | Giganti della Sila Park

## Slide 4
System Architecture Overview
Three-Tier Architecture | Edge → Fog → Cloud
EDGE TIER
S6000U Sensor (RS485/Modbus)
EG5120 Industrial Gateway
Local ML Inference
GPS GNSS Module
FOG TIER
Node-RED Orchestration Engine
InfluxDB Time-Series Database
Grafana Visualization Layer
FastAPI Backend Services
CLOUD TIER
InfluxDB Cloud (AWS)
RCMS Remote Device Management
Admin Web Platform
RAG Chatbot (Groq API)
Smart IoT Environmental Monitoring | Giganti della Sila Park

## Slide 5
Hardware: Robustel EG5120 & S6000U
Industrial IoT Gateway & Multi-Purpose Sensor
Robustel EG5120 Gateway
Edge Computing
Node-RED, InfluxDB, Grafana; Python 3; TensorFlow Lite
Industrial Reliability
-Dual SIM failover; IP30 housing
Security
IPsec, OpenVPN, Firewall; SSH/HTTPS
Protocol Gateway
Modbus RTU/ASCII; MQTT; HTTP/HTTPS; GPS NMEA
S6000U Multi-Purpose Sensor
IP65-rated • 6 sensors in 1 • RS485 Modbus RTU
Address
Parameter
Scaling
0x100
Temperature
Value / 100 (°C)
0x101
Humidity
Value (0–100%)
0x102
Light Intensity
Value (lux)
0x103
Noise Level
Value (dBA)
0x104–105
Pressure
IEEE 754 Float (hPa)
0x106
ToF Distance
Value (mm)
Smart IoT Environmental Monitoring | Giganti della Sila Park

## Slide 7
Node-RED Workflow Engine
From sensor data to cloud — 6-step pipeline
1
Data Acquisition
Modbus RTU polls S6000U every 30s over RS485. GPS service enabled via Node-RED TCP/NMEA stream.
2
Preprocessing
Decodes Modbus registers to engineering values. JSON-formats parameters. Parses GPS NMEA for lat/lon.
3
Data Fusion
Merges sensor readings with GPS coordinates into structured JSON for spatially-aware monitoring.
4
Local Storage
Writes to local InfluxDB. Enables time-series querying for Grafana. Buffers data during outages.
5
Cloud Sync
Forwards data to InfluxDB Cloud (AWS). Enables remote access & integration with admin platform.
6
ML Integration
exec node calls predictor.py — Random Forest inference on device. Result stored in InfluxDB & Firestore.
Smart IoT Environmental Monitoring | Giganti della Sila Park

## Slide 9: G R A F A N A
Grafana is an open-source analytics & monitoring platform installed in the EG5120 App Centre (MING stack). It connects to Influx DB as a data source and renders interactive, auto-refreshing dashboards.
Dashboard Import Process
Open Grafana Web Interface (port 3000)
Navigate to Dashboard → Import
Upload prepared JSON configuration file
Select Influx DB 2.0 as data source
Click Import — dashboard renders automatically

## Slide 11
ML Pipeline & Trail Recommendation
From sensor data to personalized hiking suggestions
Open-Meteo
Dataset
Programmatic
Labeling
Train Random
Forest (PC)
Export
.pkl Model
Deploy to
EG5120 (SCP)
Edge
Inference
Weather Vibe Categories
❄ Frosty — Below 0°C
🌬 Brisk — 0–10°C, High Humidity
🍂 Crisp — 0–15°C, Low Humidity
☁ Moody — 10–20°C, Very High Humidity
☀ Serene — 15–25°C, Moderate
🔆 Sun-Drenched — Above 25°C, Low Humidity
Content-Based Filtering (CBF)
1
User selects preferences: vibe, slope, width, noise tolerance
2
System builds user preference vector from Firestore trail data
3
Compute intersection per category (vibe, slope, width, noise)
4
4 category scores aggregated into final match percentage
5
Top 5 trails ranked by match score returned to user
✅ Near-perfect classification — micro avg precision / recall / F1 = 1.00 across all 6 vibe categories
Smart IoT Environmental Monitoring | Giganti della Sila Park

## Slide 13
Web Administration Platform & RAG Chatbot
Vue.js 3 Frontend + FastAPI Backend + Groq-powered RAG
⚛️ Vue.js 3 Frontend
real-time measurements from all deployed gateways
interactive GPS map of monitoring stations
historical & real-time trends
Reactive Architecture
🔧 FastAPI Backend
Data Ingestion
Influx DB Integration
RESTful API
Pydantic Validation + Auth middleware + CORS + RBAC
🤖 RAG-Based Intelligent Chatbot (Groq API)
1
Admin submits query
2
FastAPI routes request
3
InfluxDB queried
4
Constrained prompt built
5
Groq API inference
6
Response returned
Smart IoT Environmental Monitoring | Giganti della Sila Park

## Slide 16
Deployment Procedure
Two-phase deployment: Hardware → Software
🔧 Phase 1: Hardware Deployment
1
Conduct site survey
2
Mount S6000U sensor at 2–3m height with unobstructed view
3
Install EG5120 gateway in IP65 weatherproof enclosure
4
Connect RS485 cable (max 1,200m run) and DC 12–24V power
5
Insert SIMs, attach 4G/5G and GPS antennas
6
Power on and verify LED status indicators
💻 Phase 2: Software Deployment
Step 1 — Model Transfer
Random Forest exported as .pkl
predictor.py prepared → SCP upload to EG5120
Step 2 — Edge Integration
Model stored on gateway
Node-RED collects data → Python inference
Step 3 — Data Pipeline
Sensor → Node-RED → Random Forest → InfluxDB → Grafana
✅ Validation:
Modbus → InfluxDB → Grafana → Cloud → ML → Web Platform
Smart IoT Environmental Monitoring | Giganti della Sila Park

## Slide 17
Conclusion & Future Work
What We Built
This project demonstrates a scalable IoT-based environmental monitoring system using the Robustel EG5120 gateway and S6000U sensor with edge machine learning. It enables real-time data collection, intelligent processing, and cloud integration, proving the feasibility of reliable edge-based environmental analytics.
🚀 Future Work
Mobile App for visitors with real-time trail recommendations And Real-time updates
📦 github.com/yonasyifter/IoT_ProjectWeatherForcast
Smart IoT Environmental Monitoring | Giganti della Sila Park